## Slide 1: Review: Reaction Rates and Rate Laws
Reaction rate is a function of temperature and concentration
Elementary reaction
  Involves only 1 step and proceeds as written
  Stoichiometric coefficients in an elementary reaction are identical to the powers in the rate law
  αA +βB → χC -rA = kACAαCBβ
Non-elementary reaction
  Overall equation describes the overall reaction stoichiometry and do NOT proceed as written (have multiple steps)
  Cannot identify reaction order from the overall reaction equation
  Specific rate constant depends on temperature and follows Arrhenius Eq
    To determine E, plot ln k vs 1/T for several T. Slope is –E/R
    k(T) can be determined if k(T0) is known
Taking ln of both sides:

## Slide 2: Review: Reversible Reactions
KC: concentration equilibrium constant (capital K)
At equilibrium, the reaction rate is zero, rA=0
Thermodynamic equilibrium relationship
KC is temperature dependent (no change in moles or DCP):
DHRX: heat of reaction
If KC is known for temperature T1, KC for temperature T can be calculated

## Slide 3: Review: Conversion is Everything!
Batch:
  We need to determine how long to leave the reactants in the reactor to achieve a certain conversion X
CSTR:
  We need to determine the reactor size (volume) required to achieve a certain conversion X
PFR:
  We need to determine the reactor size (volume) required to achieve a certain conversion X
-1/rA
X
-1/rA
X
But rA depends on Cj, and Cj is a function of XA
→ We need to relate rA to XA

## Slide 4: Review: Derive –rA = f(XA)
Relate all V(u) to XA
Put together
Relate all rj to Cj
nj ≡ stoichiometric coefficient
Relate all Cj(XA) to V(u)
 for products, ⊖ for reactants
Batch:
Flow:
Batch:
Flow:
Batch
& Flow:
Now that Cj is in terms of XA, we can write the rate law in terms of XA

## Slide 5: Chapter 3 Examples
Rate Laws and Stoichiometry

## Slide 6
The following reaction is irreversible at low temperature, but reversible at high temperature. kf and KC are known, but kb isn’t. Suggest a rate law for the high temperature reaction.
Need kb in known terms
Forward rxn rate:
Reverse rxn rate:
Put it together to get –rA:
At equilibrium, -rA = ?
-rA >0
-rA<0
-rA=0
-rA=1
None of the above

## Slide 7
The following reaction is irreversible at low temperature, but reversible at high temperature. kf and KC are known, but kb isn’t. Suggest a rate law for the high temperature reaction.
Solve for kb→
We know that:
Substitute this expression for kb into -rA
Need kb in known terms
Forward rxn rate:
Reverse rxn rate:
Put it together to get –rA:
At equilibrium, -rA = 0

## Slide 8
A = j =
CH4
What is the relationship between rCH4 and rO2?
nj =
O2
Use CH4 for basis
What is nj?
0.5
-0.5
3/2
-3/2
None of the above

## Slide 9
A = j =
CH4
What is the relationship between rCH4 and rO2?
-3/2
Negative because O2 is a reactant
nj =
Plug in:
O2 is consumed 1.5x faster than CH4
O2
Use CH4 for basis

## Slide 10
½ N2(g) + 3/2 H2(g) → NH3(g)
The formation of ammonia is to be carried out isothermally at 227◦C and with a pressure of 16.4 atm. This is an isobaric (constant pressure) flow system with equimolar feeds of N2 & H2. Assume the gas mixture behaves like an ideal gas.
Clicker Question 2: Does the volumetric flow rate, , change as a function of conversion, XA?
Yes
No
Not enough information to tell
1
1
1
change in total # moles at XA=1
total moles fed
  0, so  changes as a function of conversion

## Slide 11
Taking H2 as your basis, fill in the stoichiometric table for the rxn above
½ N2(g) + 3/2 H2(g) → NH3(g)
The formation of ammonia is to be carried out isothermally at 227◦C and with a pressure of 16.4 atm. This is an isobaric (constant pressure) flow system with equimolar feeds of N2 & H2. Assume the gas mixture behaves like an ideal gas.
Normalize in terms of H2 by multiplying the equation by ⅔:
H2 + ⅓N2 → ⅔NH3
Compound | Symbol | In | Change | Out
H2 | A |  |  | 
N2 | B |  |  | 
NH3 | C |  |  | 
Total |  |  |  | 
The feed contains equimolar amounts of N2 and H2 → FA0 = FB0
FA0
FB0
The feed does not contain product
0
2FA0
FB0=FA0
Add it up

## Slide 12
Taking H2 as your basis, fill in the stoichiometric table for the rxn above
½ N2(g) + 3/2 H2(g) → NH3(g)
The formation of ammonia is to be carried out isothermally at 227◦C and with a pressure of 16.4 atm. This is an isobaric (constant pressure) flow system with equimolar feeds of N2 & H2. Assume the gas mixture behaves like an ideal gas.
Normalize in terms of H2 by multiplying the equation by ⅔:
H2 + ⅓N2 → ⅔NH3
Compound | Symbol | In | Change | Out
H2 | A | FA0 |  | 
N2 | B | FB0=FA0 |  | 
NH3 | C | 0 |  | 
Total |  | 2FA0 |  | 
Change in H2:
Molar flow rate A leaves reactor
=
Molar flow rate A is fed to reactor
-
Molar rate A is consumed in reactor
How much A is consumed in mol/time?

## Slide 13
Taking H2 as your basis, fill in the stoichiometric table for the rxn above
½ N2(g) + 3/2 H2(g) → NH3(g)
The formation of ammonia is to be carried out isothermally at 227◦C and with a pressure of 16.4 atm. This is an isobaric (constant pressure) flow system with equimolar feeds of N2 & H2. Assume the gas mixture behaves like an ideal gas.
Normalize in terms of H2 by multipyling the equation by ⅔:
H2 + ⅓N2 → ⅔NH3
Compound | Symbol | In | Change | Out
H2 | A | FA0 | -FA0XA | 
N2 | B | FB0=FA0 |  | 
NH3 | C | 0 |  | 
Total |  | 2FA0 |  | 
Change in H2:
Change in N2:
Change in NH3:
-⅔FA0XA
Add up the total change

## Slide 14
Taking H2 as your basis, fill in the stoichiometric table for the rxn above
½ N2(g) + 3/2 H2(g) → NH3(g)
The formation of ammonia is to be carried out isothermally at 227◦C and with a pressure of 16.4 atm. This is an isobaric (constant pressure) flow system with equimolar feeds of N2 & H2. Assume the gas mixture behaves like an ideal gas.
Normalize in terms of H2 by multipyling the equation by ⅔:
H2 + ⅓N2 → ⅔NH3
Compound | Symbol | In | Change | Out
H2 | A | FA0 | -FA0XA | 
N2 | B | FB0=FA0 | -(⅓FA0XA) | 
NH3 | C | 0 | ⅔FA0XA | 
Total |  | 2FA0 |  | 
←H2 Out
N2:
NH3:
-⅔FA0XA
←N2 Out
←NH3 Out
FA0-FA0XA
FA0-(⅓FA0XA)
⅔FA0XA
FA0(2-⅔XA)
Add up the total change
FB0=FA0
0
H2:

## Slide 15
The formation of ammonia is to be carried out isothermally at 227◦C and with a pressure of 16.4 atm. This is an isobaric (constant pressure) flow system with equimolar feeds of N2 & H2. Assume the gas mixture behaves like an ideal gas.
H2 + ⅓N2 → ⅔NH3
Compound | Symbol | In | Change | Out
H2 | A | FA0 | -FA0XA | FA0-FA0XA
N2 | B | FB0=FA0 | -(⅓FA0XA) | FA0-(⅓FA0XA)
NH3 | C | 0 | ⅔FA0XA | ⅔FA0XA
Total |  | 2FA0 | -⅔FA0XA | FA0(2-⅔XA)
What are d, e, and CA0?
nc=⅔
nB=-⅓
→d = -⅔
equimolar feeds of N2 & H2→
change in total # moles at XA=1
total moles fed

## Slide 16
The formation of ammonia is to be carried out isothermally at 227◦C and with a pressure of 16.4 atm. This is an isobaric (constant pressure) flow system with equimolar feeds of N2 & H2. Assume the gas mixture behaves like an ideal gas.
H2 + ⅓N2 → ⅔NH3
Compound | Symbol | In | Change | Out
H2 | A | FA0 | -FA0XA | FA0-FA0XA
N2 | B | FB0=FA0 | -(⅓FA0XA) | FA0-(⅓FA0XA)
NH3 | C | 0 | ⅔FA0XA | ⅔FA0XA
Total |  | 2FA0 | -⅔FA0XA | FA0(2-⅔XA)
What are d, e, and CA0?
d = -⅔
N2 & H2 are equimolar in the feed:→
Don’t have FA0 or u0
Do have P & T
This is CT0! How is NA0 related to NT0?
P= 16.4 atm; T= 227◦C=500K
Plug in:
Relate P&T to CA0:
We divided by P 2 instead of multiplying it by 0.5

## Slide 17
ideal
The formation of ammonia is to be carried out isothermally at 227◦C and with a pressure of 16.4 atm. This is an isobaric (constant pressure) flow system with equimolar feeds of N2 & H2. Assume the gas mixture behaves like an ideal gas.
H2 + ⅓N2 → ⅔NH3
Compound | Symbol | In | Change | Out
H2 | A | FA0 | -FA0XA | FA0-FA0XA
N2 | B | FB0=FA0 | -(⅓FA0XA) | FA0-(⅓FA0XA)
NH3 | C | 0 | ⅔FA0XA | ⅔FA0XA
Total |  | 2FA0 | -⅔FA0XA | FA0(2-⅔XA)
What are the concentrations of H2, N2, and NH3 when H2 is 60% consumed?
1
1
1
isothermal
isobaric
CC0=0

## Slide 18
A reversible reaction is carried out in a CSTR. What is the CSTR volume when XA=0.9, CA0=2 mol/m3, FA0=2 mol/min, and there is no product in the feed stream?
A
A + B
Check if XA=0.9 is obtainable by determining XA when the rxn is at equilibrium (-rAe=0):
Rearrange
Put CAe and CBe in terms of XAe:
Plug CAe and CBe into rate eq:
XAe =2 or XAe=0.5
Plug in values of variables & simplify
X
Impossible
0.5 =XAe< XA=0.9
Cannot obtain XA of 0.9!